Figure 1 Gary Galo's and D.M. Shields's bass correction network, see Gary Galo, "An archival phono preamplifier", Linear Audio vol. 5, pages 77...104

Assumptions: everything ideal, gain doesn't matter much, the zero and the pole realized by this circuit have to be very accurately put on certain desired locations by setting R4 and R5 (all other component values are fixed in Gary Galo's design).

I_"out" = V_{"in"} over {R_6} + V_{"in"} {{ R_4 } over { R_3 + R_4 }} cdot {{1} over { s {R_3 R_4} over {R_3 + R_4} C_1 + 1 }} cdot A cdot {1 over { R_5 }}

{I_"out"} over V_{"in"} = 1 over {R_6} + {{ R_4 } over { R_3 + R_4 }} cdot {{1} over { s {R_3 R_4} over {R_3 + R_4} C_1 + 1 }} cdot A cdot {1 over { R_5 }}

where A = 1 + R1/R2.

The pole lies at s = -{{ 1 } over { {{R_3 R_4} over {R_3 + R_4} C_1} }} . The second term of the expression for Iout/Vin goes to infinity for s approaching this value, the first term stays finite, so the sum also goes to infinity. Hence, the first corner frequency is F_3 = {{ 1 } over {2 %pi {{R_3 R_4} over {R_3 + R_4} C_1} }} and the first time constant T_3 = {R_3 R_4} over {R_3 + R_4} C_1 , exactly as described by Gary Galo. Rearranging this last equation results in his equation R_4 = {R_3 T_3} over {R_3 C_1 - T_3} .

When the zero is called sz, by definition, at s = sz, the transfer is zero. Hence,

0 = {1} over {R_6} + {{ R_4 } over { R_3 + R_4 }} cdot {{1} over { s_"z" {R_3 R_4} over {R_3 + R_4} C_1 + 1 }} cdot A cdot {1 over { R_5 }}

Multiplying everything by R5 and putting one term on the other side of the equal sign:

{R_5} over {R_6} = - {{ R_4 } over { R_3 + R_4 }} cdot {{1} over { s_"z" {R_3 R_4} over {R_3 + R_4} C_1 + 1 }} cdot A

{R_5} over {R_6} = - {{ R_4 A } over { s_"z" R_3 R_4 C_1 + {R_3 + R_4} }}

Substituting sz = -2 π F4 to match Galo's notation:

R_5 = { R_4 R_6 A } over {2 %pi F_4 R_3 R_4 C_1 - R_3 - R_4}

Dividing numerator and denominator by R4 and writing R3C1 = 1/(2 π F3min) to make it look more like Galo's equation on page 91 of the article:

R_5 = { R_6 A } over {2 %pi F_4 R_3 C_1 - R_3 over R_4 - 1} = { R_6 A } over {{F_4 } over {F_"3min"} - R_3 over R_4 - 1}

The numerator equals the numerator of Galo's equation, the weird factor F3 + 1 in the first term of the denominator has changed into F3min and there is an extra term -R3/R4.

This extra term can be expressed as a function of F3 and F3min, if so desired. Using

R_4 = {R_3 T_3} over {R_3 C_1 - T_3}

R_3 over R_4 = {R_3 C_1 - T_3} over T_3 = {{1} over {2 %pi F_"3min"} - {1} over {2 %pi F_3}} over {{1} over {2 %pi F_3}} = F_3 left( {1 over F_"3min" - 1 over F_3} right ) = F_3 over F_"3min" - 1

one finds

R_5 = {R_6 A} over {{{F_4} over {F_"3min"}} - {R_3 over R_4} - 1} = { R_6 A } over {{{F_4} over {F_"3min"}} - {{F_3} over {F_"3min"}}}

The term - 1 in the denominator of Galo's equation has changed into - F3/F3min. As Galo never introduced a symbol for the "base frequency" F3min but used the same symbol as for F3, it is quite possible that he mixed up F3 and F3min and thought their ratio was 1.